## Slide 1
Client 1
(SIP phone)
10.8.0.11
Client 7
(local computer)
10.8.0.6
Client 3
(Asterisk)
10.8.0.8
VPN Server
(35.156.226.59)
Client 5
(SIP phone)
10.8.0.10
Client 4
(SIP phone)
10.8.0.9
Client 2
(SIP phone)
10.8.0.7
Whenever a client establishes a connection with the VPN server, the client receives an internal IP address (10.8.0.6)
If a SIP phones connects to the Asterisk server, the IP address in “sip show peer” should be the internal IP address (10.8.0.6).
How does the VPN server know to transfer packets from a SIP phone (10.8.0.11) to the Asterisk server? client-to-client

## Slide 2
Softphone
10.8.0.6
Asterisk
52.87.148.169
VPN Server
(35.156.226.59)
Secure
through vpn
Unsecure
over internet
Current situation
Softphone registered with IP address 35.156.226.59
(sip show peers)
Communication between the VPN server and Asterisk is unsecure because it runs
on the internet rather than through a VPN tunnel

## Slide 3
SIP phone
10.8.0.6
Asterisk
52.87.148.169
VPN Server
(35.156.226.59)
Secure
through VPN
Internet
Unsecure
Internet
local computer
10.8.0.7
Internet
Secure
through VPN
Ping 10.8.0.6
Ping 10.8.0.7
Configure SIP phone from browser
Current situation

## Slide 4
Softphone
10.8.0.6
VPN client
(Asterisk)
10.8.0.7
VPN Server
(35.156.226.59)
Secure
through VPN
Target situation
Softphone registered with IP address 10.8.0.6
(sip show peers)
Secure
through VPN
How important is it to make the connection
between VPN and Asterisk secure through VPN?
Not really, configuring phone through VPN is still possible.
Only communication is unsecure between VPN and Asterisk.